## Slide 1: After Shewhart
Roland Caulcutt
10 12 2024

## Slide 2: When SPC became everyone’s best friend
In the 1960s and the 1970s many products from Japan were becoming more popular than those made in “The West”.
Cameras, watches and cars from Japan were threatening to flood the British market.
The government publicised the Japanese threat ….
This helped to fuel a demand for training courses in Statistical Process Control within British manufacturing companies.
Many available courses were offered by trainers who had studied the writings of Shewhart and his followers, including Deming, Wheeler, Duran and Crosby.

## Slide 3: An unhappy employee
In 1988 a process operator, in the chemical industry, told me that some SPC charts “were ridiculous”.
On day 4, we measure the quality, then we take action
He explained to me that his supervisor insisted on the operators following, what he called, the Shewhart procedure:
On day 1, we measure the quality
On day 2, we measure the quality
On day 3, we measure the quality
we plot the mean of the four measurements on the mean chart
we plot the range of the four measurements on the range chart

## Slide 4: Shewhart’s procedure had worked well in Bell Telephone Laboratories
Telephones were made by assembling components.
It was in the assembly industries that Shewhart’s procedures for quality control had proved to be very useful.
However, many of the companies I visited, were struggling to make Shewhart’s mean and range charts, work with their continuous processes that give one-at-a-time data
Shewhart’s data was in natural groups, often groups of four.

## Slide 5: The supervisor’s understanding of SPC
I learned that the supervisor had attended an SPC course.
Perhaps that course was OK for the assembly industries, but was not suitable for the process industries.
I advised the process operator that an Individuals chart would be more suitable. It would allow him to plot a point every day.
But the supervisor told the operator to continue with the mean chart, because it was more powerful than the individuals chart.

## Slide 6: One-at-a-time data ……. Process times
Number Time Number Time Number Time
1 74 18 95 35 91
2 91 19 72 36 80
3 84 20 90 37 75
4 82 21 81 38 68
5 64 22 97 39 88
6 76 23 83 40 63
7 80 24 73 41 72
8 81 25 71 42 86
9 83 26 86 43 83
10 75 27 89 44 81
11 83 28 74 45 81
12 86 29 90 46 75
13 70 30 92 47 79
14 82 31 82 48 68
15 76 32 95 49 79
16 101 33 73 50 77
17 87 34 79
This is
One-at-a-time
data

## Slide 7: An individuals chart of the process times

## Slide 8: Increasing the power of the individuals chart
The individuals chart will detect process changes more quickly if we:
add warning lines
add additional decision rules
calculate means
The moving mean chart and the exponentially weighted moving mean chart became popular in the 1990s.
But many people using these moving mean charts, did not realise that a series of moving means will be autocorrelated.

## Slide 9: Positive autocorrelation

## Slide 10: Negative autocorrelation

## Slide 11: A test for autocorrelation
No of points 10 12 14 16 18 20 22 24 26 28 30 32 34 36 38
Lower limit 3 3 4 5 6 6 7 8 9 10 11 11 12 13 14
Upper limit 8 10 11 12 13 15 16 17 18 19 20 22 23 24 25
No of points 40 42 44 46 48 50 60 70 80 90 100 110 120
Lower limit 15 16 17 17 18 19 24 28 33 37 42 46 51
Upper limit 26 27 28 30 31 32 37 43 48 54 59 65 70
Count the number of times the data plot crosses the centre line.
If this number is less than the lower limit …....... We have Positive autocorrelation
If this number is more than the upper limit ….. We have Negative auto correlation

## Slide 12
I showed the supervisor a British Standard containing several charts that other people use.
BS ISO 7870 Control Charts
BS ISO 7870 Part 1 - General Guidelines - 2019
BS ISO 7870 Part 2 - Shewhart Control Charts - 2023
BS ISO 7870 Part 3 - Acceptance control charts - 2020
BS ISO 7870 Part 4 - Cusum charts - 2021
BS ISO 7870 Part 5 - Specialised control charts - 2014
BS ISO 7870 Part 6 - EWMA control charts - 2016
BS ISO 7870 Part 7 - Multivariate control charts - 2020
BS ISO 7870 Part 8 - Short run control charts - 2017
BS ISO 7870 Part 9 - Auto correlation control charts - 2020

## Slide 13: Èxponentially weighted moving average chart (EWMA)
New plot = Sc(New data) + (1-Sc) (Old plot)
Sc = Smoothing constant ,,,,,,, A number between 0 and 1
The plotted points will be positively autocorrelated.
So the decision lines are adjusted, accordingly.

## Slide 15: A cusum chart of DPMO data

## Slide 16: Interpreting a cusum chart
If part of a cusum chart has a downward slope,
the data is below target during that period.
If part of a cusum chart has an upward slope,
the data is above target during that period.
If part of a cusum chart is horizontal, the
data is on target.
Where the cusum chart has a slope change, the
data has a change in mean level.

## Slide 17: Changes detected by the Cusum chart

## Slide 18: Comparing the performance of alternative charts
All control charts will give you false signals:
False negatives
False positivies.
In practice you want to see:
An early signal, when a real change occurs.
Very few signals, whilst the process is stable.
The performance of a control chart can be assessed by measuring its average run length.

## Slide 19: The performance of control charts

## Slide 20: What do process managers want?
For detecting a change of mean equal to one standard deviation, the Cusum is very powerful.
Many managers wish to get early warning of changes, that are equal in size to one standard deviation.
But managers don’t want lots of false alarms.
Managers don’t want mathematics or statistical jargon

## Slide 21: One hundred years ago, time flowed slowly. Today it has flown.
Thank you for your attention.
I’m sorry my presentation was so hurried.
In the concluding session you will be able to question the speakers.